## Slide 1: ECE 383 – Embedded Computer Systems II Lecture 1 – Intro to Digital System Design
Capt Jeffrey Falkinburg Room 2E46C 333-7366
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Computer Engineering Courses
ECE 281:
Digital Design &
Comp Arch
ECE 382:
Embedded Comp
Systems I
ECE 383:
Embedded Comp
Systems II
ECE 484:
Adv Digital
System Design
ECE 485:
Adv Computer
Architecture
ECE 387:
Introduction to
Robotics

## Slide 3: Lesson Outline
Why digital systems?
Instructor/Course Introduction
Methods of implementing digital systems
Custom digital device technologies
Abstraction
Digital System Design
Design Goals
Digital Design – Majority Circuit

## Slide 4: Why Digital Systems?

## Slide 5: Why Digital Systems?
Advantages
  Reproducibility of information
  Flexibility and functionality: easier to store, transmit and manipulate information
  Economy: cheaper device and easier to design
Digital circuitry replaces many analog systems:
  Audio recording: from tape to music CD to MP3 (MPEG Layer 3) player
  Image processing: from silver-halide film to digital camera
  Telephone switching networks
  Control of mechanical system: e.g., “fly-by-wire”

## Slide 6: Why Digital Systems?
Fly-By-Wire Digital System

## Slide 7: Instructor/Course Intro

## Slide 8
About me…
Education
  BSCE, University of Nebraska Lincoln – Omaha Campus
  MSCE, Air Force Institute of Technology (AFIT)
USAF Career (62E3C, T62E3E, 62E3A, 3CO31, 2E231)
  Prior Enlisted 9.5 yrs
    3rd Combat Communication Group – Tinker AFB, OK
      Operation Southern Watch – Eskan Village, Saudi Arabia
    55th Communications Group – Offutt AFB, NE
    School/AFROTC/AECP – University of Nebraska
  Air Force Research Labs (AFRL) – Munitions Directorate – Eglin AFB, FL
    Operation Iraqi Freedom – Al Asad, Iraq
  School – AFIT
  711 Human Performance Wing (HPW) – Wright Patterson AFB, OH
Interests - Spending time with my Family, computers, watching movies, woodworking, getting outside

## Slide 9: The Family

## Slide 10: Information Sheet
Name
Hometown
Hobbies / Interests
Course Goals?
Issues / Concerns about this course?
Anything else I should know?

## Slide 11: Extra Instruction (EI)
M1
ECE 383 – 2E48A
M6
M7
M5
T1
T5
T6
T7
M3
ECE 463 – 2G2
M4
ECE 463 – 2G2
T2
T3
ECE 281 – 2F44
T4
Capt Jeffrey Falkinburg
2E46C
Office: 333-7366
Sometimes Available
Available
Always Unavailable
M2
ECE 383 – 2E48A

## Slide 12
West (Terrazzo) Side

## Slide 13
Why I do what I do

## Slide 14: Rules
Be prepared for class (reading/homework)
Pay attention in lecture (1st hour)
Be productive during 2nd hour of application

## Slide 15: Course Materials
Website:
  http://ece.ninja/383/
Textbook:
  RTL Hardware Design Using VHDL
  Pong P. Chu

## Slide 16: Methods of implementing digital systems

## Slide 17: Digital Implementation Methods
General-purpose hardware with custom software
  General purpose processor
    Performance-oriented processor (e.g., Core i7)
    Cost-oriented processor (e.g., PIC microcontroller)
  Special purpose processor
    DSP processor (multiplication-addition)
    Network processor (buffering and routing)
    Graphics engine (3D rendering)
Custom software on a custom processor (known as hardware-software co-design)
Custom hardware
Note: A complex project may use more than one of these!

## Slide 18: Digital Implementation Methods
General Purpose Hardware
Custom Software
Custom Hardware
Custom Software
Custom Hardware
Increasing Cost
Increasing Development Time
Increasing Performance
Increasing Power Consumption

## Slide 19: Custom digital device technologies

## Slide 20: Custom Digital Device Technologies
Where customization is done:
  In a fab (fabrication facility): ASIC (Application Specific IC)
  In the “field”: non-ASIC
Six device technology classifications:
  Full-custom ASIC
  Standard cell ASIC
  Gate array ASIC
  Complex field programmable logic device
  Simple field programmable logic device
  Off-the-shelf SSI (Small Scaled IC)/MSI (Medium Scaled IC) components

## Slide 21: Full-custom ASIC
All aspects (e.g., size of a transistor) of a circuit are tailored for a particular application.
Circuit fully optimized
Design extremely complex and involved
Only feasible for small components
Masks needed for all layers
Full-Custom ASIC
Standard-Cell ASIC
Gate-Array ASIC
Complex PLDs
Simple PLDs
SSI/MSI

## Slide 22: Standard-Cell ASIC
Circuit made of a set of pre-defined logic, known as standard cells
  Basic logic gates
  1-bit adder,
  D FF
  etc.
Layout of a cell is pre-determined, but layout of the complete circuit is customized
Masks needed for all layers
Full-Custom ASIC
Standard-Cell ASIC
Gate-Array ASIC
Complex PLDs
Simple PLDs
SSI/MSI

## Slide 23: Gate array ASIC
Circuit is built from an array of a single type of cell (known as base cell)
Base cells are pre-arranged and placed in fixed positions, aligned as one- or two-dimensional array
More sophisticated components (macro cells) can be constructed from base cells
Masks needed only for metal layers (connection wires)
Full-Custom ASIC
Standard-Cell ASIC
Gate-Array ASIC
Complex PLDs
Simple PLDs
SSI/MSI

## Slide 24: Complex Field Programmable Device
Device consists of an array of generic logic cells and general interconnect structure
Logic cells and interconnect can be “programmed” by utilizing semiconductor fuses or switches
Customization is done “in the field” vs. fab
Two categories:
  CPLD (Complex Programmable Logic Device)
  FPGA (Field Programmable Gate Array)
No custom mask needed
Full-Custom ASIC
Standard-Cell ASIC
Gate-Array ASIC
Complex PLDs
Simple PLDs
SSI/MSI

## Slide 25: Simple Field Programmable Device
Programmable device with simple internal structure
  PROM (Programmable Read Only Memory)
  PAL (Programmable Array Logic)
  etc.
No custom mask needed
Replaced by CPLD/FPGA
Full-Custom ASIC
Standard-Cell ASIC
Gate-Array ASIC
Complex PLDs
Simple PLDs
SSI/MSI

## Slide 26: SSI/MSI components
Small parts with fixed, limited functionality
  7400 TTL series (more than 100 parts)
  etc.
Resource is consumed by package but not silicon:
  Power
  Board area
  Manufacturing cost
  etc.
No longer a viable option
Full-Custom ASIC
Standard-Cell ASIC
Gate-Array ASIC
Complex PLDs
Simple PLDs
SSI/MSI

## Slide 27: Types of Cost
  NRE (Non-Recurrent Engineering) cost: one-time, per-design cost
  Part cost: per-unit cost
  Time-to-market cost: loss of revenue

## Slide 28: Technology Summary
Trade-off between optimal use of hardware resource and design effort/cost
No single best technology

## Slide 29: Abstraction

## Slide 30: Digital System Views
Behavioral view:
  Describe functionalities and I/O behavior
  Treat the system as a black box
Structural view:
  Describe the internal implementation (components and interconnections)
  Essentially block diagram
Physical view:
  Add more info to structural view: component size, component locations, routing wires
  E.g., layout of a print circuit board

## Slide 31: Register-Transfer Abstraction
Contains higher-level components (register, adder, mux, etc.) – think of datapaths in ECE 281/382
Based on clock “tick” event
Described as a finite state machine
Later on: a design methodology in which the system operation is described by how the data is manipulated and moved among registers

## Slide 32: Digital system design

## Slide 33: VHDL Design
VHDL is just a language which is used to describe hardware circuits.
A piece of hardware is described in VHDL in two separate ways.
  Entity – Describes the inputs and outputs
  Architecture – Describes what transformation the box performs.
There are two good reasons to realize a design in VHDL, you can simulate and synthesize hardware specified.

## Slide 34: Digital System Simulation
Simulation
  When a design is simulated you have complete control of time and the values of all the signals (wires) in the design.
  Aids in Debugging
  We will use Xilinx lSim to perform our VHDL simulations.

## Slide 35: Digital System Implementation
Synthesis
  Maps a higher-level description to lower-level components (RT, gate, technology map levels)
  Results in structural view
Physical Design
  Generates netlist based on synthesis
  Floor Plan – layout based on RT/processor level
  Place & Route – gate level
  Circuit Extraction – Compute propagation delays (Cp/R)
  Power/Clock Networks
  Etc.

## Slide 36: Digital System Implementation
Verification – Checking whether a design meets the functional and timing goals
  Simulation
  Formal verification
  Hardware emulation
Testing – Process of detecting physical defects of a die or package that occurred during manufacturing

## Slide 37: Design goals

## Slide 38: Design Goals
Design for Efficiency
  Synthesis cannot convert bad designs into good ones
  Know what hardware your HDL will create
Design for Large
  Design a large module
  Design to be incorporated into a larger system
  Design to facilitate the overall development process
Design for Portability
  Device independent
  Software independent
  Design reuse

## Slide 39: Digital Design – Majority Circuit

## Slide 40: Digital Design – Majority Circuit
Word Statement: Build a circuit (SOP min) with 3-bits of input and 1-bit of output. The output equals 1 when a majority of the three inputs equal 1.
Abstract word or statement
Truth
Table
Symbolic
Circuit Design Diagram
VHDL

## Slide 41: Important Notes
You can use all the standard logic gates including:
  AND
  OR
  XOR
  NAND
  NOR
  XNOR
  NOT

## Slide 42: Important Notes
The "data type" std_logic can represent much more than just a logic 0 or 1.
  'U', -- Uninitialized
  'X', -- Forcing Unknown
  '0', -- Forcing 0
  '1', -- Forcing 1
  'Z', -- High Impedance
  'W', -- Weak Unknown
  'L', -- Weak 0
  'H', -- Weak 1
  '-' -- Don't care

## Slide 43: Lesson Outline
Why digital systems?
Instructor/Course Introduction
Methods of implementing digital systems
Custom digital device technologies
Abstraction
Digital System Design
Design Goals
Digital Design – Majority Circuit