## Slide 1: Interpolation Block Diagram
8
Phase Inc
Interpolated Value
= Base + (Next – Base) * Offset
Q4.4
8
8
8
Index.Offset
cw0
Q4.4
8
8
8
4
Index
‘1’
Mux
cw1
4
1
0
Index
4
Offset
4
8
Addr
BRAM
‘1’
Data
Read
8
Base
Base Value
cw2
8
Next
Next Value
cw3
Next
Base
8
8
Offset
4
8
13
Q9.4
Base
delta*offset
Remove ‘0’ & truncate
delta
Switches
8
8
8
Switches
Amplify
8
Q8.0
BRAM is assumed to be signed. If not, convert from unsigned to sign after reading value
WARNING: Our VHDL does signed multiplies, not unsigned multiplies
If a value is unsigned, like Offset and Amplify,
you will need to fool the multiply by appending a ‘0’ to the MSB,
And then remove the MSB from the answer. If both inputs are unsigned, you’ll need to remove two ‘00’s from the MSB of the answer
WARNING: This data flow is assumed for “signed” sine wave, not “unsigned”
Q8.0
Q17.0
Q8.0
Q0.4
18 or 16 MSBs?
Q8.0
signed
Append ‘0’ MSb
Q8.0
5
Q1.4
X
-
X
Q8.0
Q8.0
Q8.0
Interpolated Value
Q8.0
Amplify By
8
9
Append ‘0’ MSb
remove ‘0’ & truncate
17
16
Q16.0
Amplified_Interpolated Output
signed
Uninterpolated Output
signed
Base
+ -