## Slide 1
ECE 383 – Embedded Computer Systems II Lecture 18 – Soft Core (MicroBlaze) + Custom IP
1
Maj Jeffrey Falkinburg Room 2E46E 333-9193

## Slide 2: Lesson Outline
Time Logs!
MicroBlaze + Custom IP

## Slide 3: MicroBlaze + Custom IP

## Slide 4: MicroBlaze + Custom IP
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
Lec18.c
my_counter_ip_v1_0.vhd @ 0x44a00000
axi_lite
my_counter_ip_v1_0_S00_AXI.vhd
Lec18.vhd
32
slv_reg0
Q/D
32
Lec18.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
slv_reg2

## Slide 5: MicroBlaze + Custom IP
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg1
clk
reset_n
ctrl
Artix 7 (design_1)
MicroBlaze
Lec19.c
my_counter_ip_v2_0.vhd @ 0x44a00000
axi_lite
my_counter_ip_v2_0_S00_AXI.vhd
Lec18.vhd
32
slv_reg0
Q/D
32
Lec18.xdc
8
LED
T14
T15
T16
U16
V15
W16
W15
Y13
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
roll
Interrupt
myISR()
main()

## Slide 6: MicroBlaze + Custom IP

## Slide 7: MicroBlaze + Custom IP – Workflow
The work flow has three main steps.
  Define a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator
  Create and package new custom IP (your custom hardware) and import it into your Vivado design
  Program the resulting hardware in the SDK environment.
Lets start with the first step.

## Slide 8: Xilinx Vivado – IP Integrator
  This step requires that you start a new hardware design (MicroBlaze + axi_uartlite) in Vivado IP Integrator in a new project called Lecture_18.
  You will add a new Block Design with a MicroBlaze and axi_uartlite following the MicroBlaze Tutorial.
https://reference.digilentinc.com/learn/programmable-logic/tutorials/nexys-video-getting-started-with-microblaze/start

## Slide 9: Xilinx Vivado – Create and Package Custom IP
  This step requires Create and package new custom IP (your custom hardware) and import it into your Vivado design.
  You will defined the logical arrangement of the component in VHDL. Your entity description will contain two types of connections; those targeted at external ports on the Artix 7 chip and those intended to be accessible to the MicroBlaze processor.
  You can also use this online tutorial to help guide you.
  https://reference.digilentinc.com/learn/programmable-logic/tutorials/zedboard-creating-custom-ip-cores/start

## Slide 10: Xilinx Vivado – Create and Package Custom IP
1. Open Vivado and create a new project
  Go to Tools→Create and package IP

## Slide 11: Xilinx Vivado – Create and Package Custom IP
2. Create your custom IP project
  2.1) Select Create a new AXI4 peripheral and click Next

## Slide 12: Xilinx Vivado – Create and Package Custom IP
  2.2) Input “My_Counter_IP” in the name field and click Next

## Slide 13: Xilinx Vivado – Create and Package Custom IP
  2.3) Change the number of Registers to 32 on the AXI interface and click Next

## Slide 14: Xilinx Vivado – Create and Package Custom IP
  2.4) Select Edit IP and click Finish

## Slide 15: Xilinx Vivado – Create and Package Custom IP
3. Designing the IP core
  3.1) A new instance of Vivado will open up for the new IP core. Expand the top level file My_Counter_IP_v1_0. Then double-click on My_Counter_IP_v1_0_S00_AXI to open it in the editor.

## Slide 16: Xilinx Vivado – Create and Package Custom IP
4. Adding the Lec 10 Counter to the My_Counter_IP_v1_0 project by adding the source lec18.vhd file
  Your counter will not yet be connected to the top level design

## Slide 17: Part 1a: Hardware Questions/ Notes related to handout
Note: the truth table for the counter is in the comments.
Q: In lec18.vhdl, what other library must be added?
Q: In lec18.vhdl, does the use work.lec18Parts.all library need to be added?

## Slide 18: MicroBlaze + Custom IP

## Slide 19: Lec18.vhdl – Lec 10 Counter

## Slide 20: Part 1b: Hardware Questions/ Notes related to handout
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what do the generics C_NUM_REG, C_SLV_DWIDTH do?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what two roles is slv_reg0 serving?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, what roles does slv_reg1 serve?
Q: In my_counter_ip_v1_0_S00_AXI.vhd, slv_reg0 is on the left and right-hand side of an assignment. Identify the two lines where this happens.
Q: In my_counter_ip_v1_0_S00_AXI.vhd, on line 62, what is the role does X"000000" serve?

## Slide 21: MicroBlaze + Custom IP

## Slide 22: my_counter_ip_v1_0_S00_AXI.vhd – User Logic

## Slide 23: my_counter_ip_v1_0_S00_AXI.vhd – User Logic

## Slide 24: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add numeric standard library at the top of the file:
  use ieee.numeric_std.all;

## Slide 25: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add a port for the LEDs in the my_counter_ip_v1_0_S00_AXI entity between the comments:
  port (
  -- Users to add ports here
  LED : out std_logic_vector(7 downto 0);
  -- User ports ends
  -- Do not modify the ports beyond this line
  -- Global Clock Signal
  S_AXI_ACLK : in std_logic;

## Slide 26: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add the counter declaration and a signal for Q before begin in the my_counter_ip_v1_0_S00_AXI architecture:
  component lec10 is
  generic (N: integer := 4);
  Port( clk: in STD_LOGIC;
  reset_n : in STD_LOGIC;
  roll : out STD_LOGIC;
  ctrl: in std_logic_vector(1 downto 0);
  D: in unsigned (N-1 downto 0);
  Q: out unsigned (N-1 downto 0));
  end component;
  signal Q : unsigned (7 downto 0);

## Slide 27: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Add the counter implementation and connect the wires within the my_counter_ip_v1_0_S00_AXI architecture:
  -- Add user logic here
  counter: lec10
  generic map (8)
  port map( clk => S_AXI_ACLK,
  reset_n => S_AXI_ARESETN,
  roll => roll_sig,
  ctrl => slv_reg1(1 downto 0),
  D => unsigned(slv_reg0(7 downto 0)),
  Q => Q);
  LED <= std_logic_vector(Q);

## Slide 28: Xilinx Vivado – Create and Package Custom IP
5. Modifying My_Counter_IP_v1_0_S00_AXI axi bus interface file
  Connect the counter implementation Q output signal to slave register 0 (slv_reg0) in the my_counter_ip_v1_0_S00_AXI architecture:
  loc_addr := axi_araddr(ADDR_LSB + OPT_MEM_ADDR_BITS downto ADDR_LSB); case loc_addr is
  when b"00000" =>
  reg_data_out <= x"000000" & std_logic_vector(Q);
  when b"00001" =>
  reg_data_out <= slv_reg1;
  when b"00010" =>
  reg_data_out <= slv_reg2;

## Slide 29: Part 1c: Hardware Questions/ Notes related to handout
Q: If you want a signal to go outside the Artix 7 chip...
  What files must it appear on the entity description?
  What other files must contain information about the signal?
Q: If you want a signal to go to the MicroBlaze...
  What files must it appear on the entity description?
  In order for the MicroBlaze to read the signal, what must you do?
  In order for the MicroBlaze to write to the signal, what must you do?

## Slide 30: MicroBlaze + Custom IP

## Slide 31: My_Counter_IP_v1_0.vhd – Top Level

## Slide 32: My_Counter_IP_v1_0.vhd – Top Level

## Slide 33: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add numeric standard library at the top of the file:
  use ieee.numeric_std.all;

## Slide 34: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port for the LEDs in the my_counter_ip_v1_0 entity between the comments to expose it to externally:
  port (
  -- Users to add ports here
  LED : out std_logic_vector(7 downto 0);
  -- User ports ends
  s00_axi_aclk : in std_logic;

## Slide 35: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port for the LEDs in the my_counter_ip_v1_0_S00_AXI component declaration:
  port (
  LED : out std_logic_vector(7 downto 0);
  S_AXI_ACLK : in std_logic;

## Slide 36: Xilinx Vivado – Create and Package Custom IP
6. Modifying My_Counter_IP_v1_0 top level file
  Add a port map for the LEDs in the my_counter_ip_v1_0_S00_AXI component instantiation:
  port map (
  LED => LED,
  S_AXI_ACLK => s00_axi_aclk,

## Slide 37: Xilinx Vivado – Create and Package Custom IP
7. Packaging the IP core
  Now that we have written the core, it is time to package up the HDL to create a complete IP package.
  7.1) Now click on Package IP in the Flow Navigator and you should see the Package IP tab. Select Compatibility and make sure “Artix7” are present. If those are not there, you can add them by clicking the plus button. The Life Cycle does not matter at this point.

## Slide 38: Xilinx Vivado – Create and Package Custom IP
7. Packaging the IP core

## Slide 39: Xilinx Vivado – Create and Package Custom IP
7.2) Select Customization Parameters and select the line for Merge Changes from Customization Parameters Wizard. This will have the My_Counter_IP parameters from the top file.

## Slide 40: Xilinx Vivado – Create and Package Custom IP
7.3) Select Customization GUI. This is were we get to change our graphical interface. No changes at this time.

## Slide 41: Xilinx Vivado – Create and Package Custom IP
7.4) Now the core should be complete so select Review and Package and click the Re-package IP button.

## Slide 42: Xilinx Vivado – Create and Package Custom IP
7.5) A popup will ask if you want to close the project, Select Yes.

## Slide 43: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.1) In the project manager page of the original window, click Open Block Design. This adds a block design to the project.
  8.2) Use the Add IP button to add our Lec 10 Counter IP Core.

## Slide 44: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.3) Right click on LEDs and select Make External.

## Slide 45: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.4) The MIG block should read my_counter_ip_0. Place your cursor on this symbol || next to the LED[7:0] port name. Your cursor will change to look like a pencil. Right click here and in the drop down list select Make External or left click on || and use the keyboard shortcut, “Ctrl+t”.

## Slide 46: Xilinx Vivado – Create and Package Custom IP
8. Add Custom IP to your design
  8.5) Your custom IP should now be connected. Now you need to add a constraints file to add the LED net to the pins on the Artix 7 chip by adding the following lines to the Lec18.xdc file.
  ## LEDs
  set_property -dict { PACKAGE_PIN T14 IOSTANDARD LVCMOS25 } [get_ports { LED[0] }]; #IO_L15P_T2_DQS_13 Sch=led[0]
  set_property -dict { PACKAGE_PIN T15 IOSTANDARD LVCMOS25 } [get_ports { LED[1] }]; #IO_L15N_T2_DQS_13 Sch=led[1]
  set_property -dict { PACKAGE_PIN T16 IOSTANDARD LVCMOS25 } [get_ports { LED[2] }]; #IO_L17P_T2_13 Sch=led[2]
  set_property -dict { PACKAGE_PIN U16 IOSTANDARD LVCMOS25 } [get_ports { LED[3] }]; #IO_L17N_T2_13 Sch=led[3]
  set_property -dict { PACKAGE_PIN V15 IOSTANDARD LVCMOS25 } [get_ports { LED[4] }]; #IO_L14N_T2_SRCC_13 Sch=led[4]
  set_property -dict { PACKAGE_PIN W16 IOSTANDARD LVCMOS25 } [get_ports { LED[5] }]; #IO_L16N_T2_13 Sch=led[5]
  set_property -dict { PACKAGE_PIN W15 IOSTANDARD LVCMOS25 } [get_ports { LED[6] }]; #IO_L16P_T2_13 Sch=led[6]
  set_property -dict { PACKAGE_PIN Y13 IOSTANDARD LVCMOS25 } [get_ports { LED[7] }]; #IO_L5P_T0_13 Sch=led[7]

## Slide 47: MicroBlaze + Custom IP

## Slide 48: Updating Custom IP
Right click on custom IP and click Edit in IP Packager to modify
1
2

## Slide 49: Xilinx Vivado – Create and Package Custom IP
Now that you updated the core you need to re-select Review and Package and click the Re-package IP button.

## Slide 50: Updating Custom IP
Refresh IP Catalog, Upgrade IP and then Re-Generate
1
2

## Slide 51: Export Design
Generate Design and take a coffee break while it builds

## Slide 52: Export Design
Exporting Hardware Design to SDK…be sure to include the bitstream…assuming no errors

## Slide 53: Launch SDK
Go to File and select Launch SDK and click OK.

## Slide 54: New SDK Project

## Slide 55: New SDK Project

## Slide 56: New C Source File

## Slide 57: New C Source File

## Slide 58: Lec18.c

## Slide 59: Lec18.c

## Slide 60: Lec18.c

## Slide 61: Lec18.c

## Slide 62: Lec18.c

## Slide 63: Lec18.c

## Slide 64: Part 2: Software Questions/ Notes related to handout
Why doesn't the 'c' command cause the counter to count up by 1?
On line 130, why did I subtract 0x30?
After loading the counter on line 132, something should be done that is missing.
What line of VHDL code in my_counter_ip_v1_0_S00_AXI.vhd is "activated" when line 80 executes?
What line of VHDL code in my_counter_ip_v1_0_S00_AXI.vhd is "activated" when line 141 executes?
What line of VHDL code in lec18.vhdl "activated" when line 141 executes?
What appears to be the naming convention for hardware registers?

## Slide 65: Add C code to Source File

## Slide 66: Xilinx Software Development Kit - SDK
In the SDK environment, you program the hardware built in the previous step.
The key concept here is that the peripheral defined in Vivado design are accessible through the slave registers as memory mapped devices.
Verify your my_counter_ip_v1_0 Base Address in system.hdf file is assigned to be 0x44a00000.
In the my_counter_ip_v1_0_S00_AXI.vhdl file, I (arbitrarily) assigned counter ports to slave register according to the table below.
Signal | direction | Slave Register | Address
D | Input | slv_reg0(7 downto 0) | 0x44a00000
ctrl | Input | slv_reg1(1 downto 0) | 0x44a00004
Q | Output | slv_reg0(7 downto 0) | 0x44a00000

## Slide 67: Increase Stack and Heap Size
You may have to add more Stack and Heap to your design
1
2
3

## Slide 68: Build and Export to FPGA

## Slide 69: MicroBlaze + Custom IP