## Slide 1: ECE 383 – Embedded Computer Systems II Lecture 25 – Digital Low Pass Filter
Capt Jeffrey Falkinburg Room 2E46C 333-7366
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Time Logs!
Project Proposals Due Today
Digital Low Pass Filter
  Filtering
  Low Pass Filter
  Filter Design Problems

## Slide 3: Filtering

## Slide 4: Filtering
Problem with sampling analog signal at discrete times?
  Aliasing problems with frequency folding

## Slide 5: Filtering
Frequency Folding creates problems in sampled systems like an ADC because noise anywhere in the spectrum will fold back into our sampling region as shown below

## Slide 6: Filtering
In order to address this problem we will utilize a principle called attenuation.
Attenuation - process of changing the amplitude of a waveform without changing its frequency.
Amount of attenuation is quantified in terms of decibels.
dB = 20 * log (V_out/V_in)
V_out/Vin | dB
1 | 0
1/10 | -20
1/100 | -40
1/1000 | -60
1/256 | -48.1648
1/1024 | -60.206
1/1.41254 | -3dB
1/2512 | -68dB
0.1V
48Khz

## Slide 7: Filtering Questions
Question 1: If you input a 1v sin wave into a circuit that attenuated it by -40dB, what would the amplitude of the output waveform be?
Given: dB = 20 * log (V_out/V_in)
  -40db = 20 log (V_out/1V_in)
  -2 = log (V_out/1V_in)
  V_out = 0.01

## Slide 8: Filtering Questions
Question 2: If you input a 1v sin wave into a circuit that attenuated it by -68dB, what would the amplitude of the output waveform be?3
Given: dB = 20 * log (V_out/V_in)
  -68db = 20 log (V_out/1V_in)
  -3.4 = log (V_out/1V_in)
  V_out = 0.4mV

## Slide 9: Filtering Questions
Question 3: If you reduced a signal by a factor of 1/256, how many dB would you need to attenuate it by?
Given: dB = 20 * log (V_out/V_in)
  20 log (1/256)
  -48db

## Slide 10: Low Pass Filter

## Slide 11: Low Pass Filter
We will use a circuit called a low pass filter to attenuate signals.
  You can build an analog low pass filter by putting a resistor and capacitor in parallel.

## Slide 12: Low Pass Filter
Our ATLYS boards have this circuit arrangement as shown by the pairs (R153, C43) and (R154,C44) in the schematic below.
Strategic parameters for this first order filter include...
  Corner frequency: 1/6.28*R153*C43 = 2854hz
  Roll off: -20dB/decade

## Slide 13: Low Pass Filter
For a Low Pass filter, the attenuation applied to an input signal depends on the input frequency.
Relationship is characterized in the filters frequency response graph. http://www.electronics-tutorials.ws/filter/fil10.gif

## Slide 14: Filter Design Problems

## Slide 15: Filter Design Problem
Lets test out understanding of all these concepts with a filter design problem.
1. Aliasing:
Your sampling an analog signal at 48kHz. List all the frequencies that will look like 2kHz signals.
  1st harmonic: 2kHz
  48khz-2khz = 46kHz
  2st harmonic: 48khz+2kHz=50kHz
  96khz-2khz = 94kHz
  3st harmonic: 96khz+2kHz=98kHz
  144khz-2khz = 142kHz

## Slide 16: Filter Design Problem
2. Decades:
A first-order LPF has a cutoff frequency of 2kHz. Describe the attenuation of a 80kHz input signal in decibels and as a ratio of output voltage to input voltage.
  Since a decade is a multiplicative factor of 10, we need to find how may powers of 10 you have to multiply by in order to increase 2 to 80. In order words
  2*10^x = 80, solving for X yields
  x = log_10(80/2) = 1.6 dB/decade

## Slide 17: Filter Design Problem
2. Decades Cont:
  So we know that a 80khz waveform is 1.6 decades above a 2khz waveform. Since the LPF attenutates -20db/decade, the 80khz waveform will be attenuated 1.6*-20 = -32db
  Decibels can be converted to the ratio of output/input using its definition...
  -32db = 20db log_10(V_out/V_in)
  V_out/Vin = 0.025 = 1/40

## Slide 18: Filter Design Problem
3. ADC convert:
You are working with a 10-bit ADC and would like to attenuate some frequency below 1/2 ULP. How many dB will be required to achieve this?
  A 10-bit ADC has a range of [0-1023], so half the unit of least place will be 1 part in 2048
  In terms of decibels this is 20*log_10(1/2^11) = -66dB

## Slide 19: Filter Design Problem
4. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  2nd order filter
  10-bit ADC
What is the minimum sampling rate?
  Reduce first fold-back to -66bB so that its at most 1/2ULP. Since the corner frequency is set to 2Kh, first fold-back to 2Khz must be reduced -63dB. At -40dB/decade this is 1.58 decades above 2kHz or 2kHz*10^1.58 = 76kHz.
  Thus, the minimum sampling frequency is 78Khz.

## Slide 20: Filter Design Problem
5. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  1st order filter
  8-bit ADC
What is the sampling rate?
  The underlying goal here is to reduce any noise folded back into our signal band below 1 ULP in the ADC.
  Since we are using an 8-bit ADC, we want to reduce the noise to 1/256 of the signal.
  This works out to -48dB.

## Slide 21: Filter Design Problem
5. Sampling frequency Cont:
  If we sample the signal at F_s, then the region between [F_s-2k, F_s] will get folded back into our signal band.
  Consequently, the filter has between 2k and F_s-2k to attenuate the signal.
  Since we have a first order filter, we will get -20dB of attenuation for every decade.
  Since we need -48dB, we will need 2.4 decades, or a factor of 251 over 2k or 502kHz.
  Thus we have F_s - 4k = 502k or F_s = 506kHz.

## Slide 22: Filter Design Problem
6. Sampling frequency:
Given:
  Signal of interest is 0-2KHz
  1st order filter
  10-bit ADC
What is the minimum sampling rate?
  Reduce first fold-back to -66bB so that its at most 1/2ULP. Since the corner frequency is set to 2Kh, first fold-back to 2Khz must be reduced -63dB. At -20dB/decade this is 3.15 decades above 2kHz or 2kHz*10^3.15 = 2.8Mhz
  Thus, the minimum sampling frequency is 2.8Mhz + 2Khz = 2.8Mhz Wow, what a difference that extra order in the filter made!

## Slide 23: Filter Design Problem
7. Filter specs:
Given:
  Signal of interest is 0-2KHz
  8-bit ADC
  Maximum possible sampling rate of 80KHz
What order filter do we need?
  An 8-bit ADC required -48db of attenuation to get the noise below 1ulp (unit of least position). From 2kHz to 78kHz is 1.6 decades (solve 2*10^x = 78) The roll off of an x-order LPF is -20*x db/decade.
-20*x db -48 db
------------ = ---------------  x = 1.5, so 2nd order filter is needed.
decade 1.6 decade

## Slide 24: Filter Design Problem
8. Signal bandwidth:
Given:
  16-bit ADC
  4th order filter
  Sampling frequency 250kHz
What is the maximum frequency of the signal of interest?
  A 16-bit ADC required -96db of attenuation to get the noise below 1ulp.
  Let the sampling frequency be called alpha.
  Fold back will occur at 250k - alpha.

## Slide 25: Filter Design Problem
8. Signal bandwidth Cont:
  Filter must attenuate signal over:
  alpha*10^x=250k-alpha
  log((250k-alpha)/alpha) decades
  4th order filter rolls off at -80db/decade
  -80 db -96 db
  -------- = ------------------------------
  decade log((250k-alpha)/alpha) decade
  alpha = 14.8Khz

## Slide 26: Filter Design Problem