## Slide 1: ECE 383 – Embedded Computer Systems II Lecture 24 - Direct Digital Synthesis and Linear Interpolation
Capt Jeffrey Falkinburg Room 2E46C 333-7366
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Time Logs!
Lab 3 – O’Scope Control Lab Report Due COB Today
  5 point bonus if completed by midnight 20 Mar
    Must have sent me an Issue Request to grade early for bonus
Project Proposals Due BOC LSN 25
Direct Digital Synthesis

## Slide 3: LUT – Look Up Table

## Slide 4: LUT – Look Up Table
Lets say that you wanted to compute the square root of an value using the microBlaze.
If you were lucky enough to have a compiler which provided this function you could just use the math library functions.
If on the other hand, you did not have the use of such a library, you would have to figure out a way to compute the square root.

## Slide 5: LUT – Look Up Table
There are many ways to compute the SQRT Function:
Crack open a book to find a mathematical expression
  Unfortunately this typically leads to timely computations
You could enumerate an every possible value of x and its square root.
  We could then look-up a SQRT in the table, by going to the row corresponding to the x and retrieving its value.
  This approach seems silly since it would use a lot of space
  We could reduce this space by eliminating entries
  We save space at the expense of introducing errors.
If you wanted the SQRT for x and its entry wasn’t in the table you would have to use the closest x in the table

## Slide 6: LUT – Look Up Table
A good compromise among all three of these design constraints:
  Space
  Time
  Error
Is to use Interpolation in a partial Look-Up-Table (LUT)

## Slide 7: Interpolation
"Interpolation is a mathematical method of creating missing data. ... There are many methods of interpolation, but one simple method would be to generate a new value by using the average of the value of the two values on either side of the one to be created.“
This average is also referred to as linear interpolation. For example if you have a value of x which is 1/2 way between 0 and 4 then you assume that the SQRT is 1/2 between 0 and 2.

## Slide 8: Linear Interpolation
We know that if f(x)=y and f(x+4)=z then we estimate the intermediate values of f(x+1), f(x+2), and f(x+3) by drawing a straight line between y and z and using the points on this line to estimate the function between x and x+4.
For example, let: F(8)=2.8284 and F(12)=3.4641 then
  F(9) = 2.8284 + 1/4(3.4641-2.8284) = 2.987
  F(10) = 2.8284 + 2/4(3.4641-2.8284) = 3.146
  F(11) = 2.8284 + 3/4(3.4641-2.8284) = 3.305
We understand that this is an approximation and consequently we will have error, but sometimes close is better than exact in embedded computing especially when time is of the essence.

## Slide 9: Linear Interpolation
  //----------------------------------------------
  // A code chunk to perform linear
  // interpolation of some unknown fnc at
  // x+i where i is between 0 and 4
  // inclusive. You are given that
  // f(x)=y f(x+4)=z
  // You are given i, please return f(x+i)
  //----------------------------------------------
  delta = (z-y)>>2;
  f = y + delta*i;
  It would be better to do the division by 4 (shift right by 2-bits) after the multiplication of delta*i because the difference (z-y) might be small and the division may result in a 0 value.

## Slide 10: Square Root Interpolation LUT
index | x | sqrt(x) | sqrt * 2^6 | Trunc Down | 2.6 Binary | 2.6 Hex
0 | 0 | 0 | 0 | 0 | 00.000000 | 00
1 | 4 | 2 | 128 | 128 | 10.000000 | 80
2 | 8 | 2.828427 | 181.0193 | 181 | 10.110101 | B5
3 | 12 | 3.464102 | 221.7025 | 221 | 11.011101 | DD
4 | 16 | 4 | 256 | 255 | 11.111111 | FF
Chart: True and discrete SQRT values
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
SQRT(X) | 0 | 1 | 1.4142 | 1.7321 | 2 | 2.2361 | 2.4495 | 2.6458 | 2.8284 | 3 | 3.1623 | 3.3166 | 3.4641 | 3.6056 | 3.7417 | 3.873
base | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 2.8284 | 2.8284 | 2.8284 | 2.8284 | 3.4641 | 3.4641 | 3.4641 | 3.4641

## Slide 11: Square Root Interpolation LUT
Chart: True and Apprx SQRT
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
SQRT(X) | 0 | 1 | 1.4142 | 1.7321 | 2 | 2.2361 | 2.4495 | 2.6458 | 2.8284 | 3 | 3.1623 | 3.3166 | 3.4641 | 3.6056 | 3.7417 | 3.873
base + offset*delta | 0 | 0.5 | 1 | 1.5 | 2 | 2.2071 | 2.4142 | 2.6213 | 2.8284 | 2.9873 | 3.1463 | 3.3052 | 3.4641 | 3.5981 | 3.7321 | 3.866
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
error(x) | 0 | 0.5 | 0.41421 | 0.23205 | 0 | 0.028961 | 0.035276 | 0.024431 | 0 | 0.012654 | 0.016013 | 0.011442 | 0 | 0.0074751 | 0.0096066 | 0.0069579

## Slide 12: Square Root Interpolation LUT
LUT |  |  |  |  |  | 
 |  |  |  |  | 10.6 Binary | 
index | x | sqrt(x) | sqrt * 2^6 | Trunc down | Upper 10-Bits | Lower 6-Bits
0 | 0 | 0 | 0 | 0 | 0000000000 | 000000
1 | 16 | 4 | 256 | 256 | 0000000100 | 000000
2 | 32 | 5.656854 | 362.0387 | 362 | 0000000101 | 101010
3 | 48 | 6.928203 | 443.405 | 443 | 0000000110 | 111011
4 | 64 | 8 | 512 | 512 | 0000001000 | 000000
5 | 80 | 8.944272 | 572.4334 | 572 | 0000001000 | 111100
6 | 96 | 9.797959 | 627.0694 | 627 | 0000001001 | 110011
7 | 112 | 10.58301 | 677.3123 | 677 | 0000001010 | 100101
8 | 128 | 11.31371 | 724.0773 | 724 | 0000001011 | 010100

## Slide 13: Square Root Interpolation LUT
Chart: Real and Approx SQRT

## Slide 14: Square Root Interpolation LUT
Chart: Error of 8 point SQRT LUT

## Slide 15: Practice
0 | 127
1 | 175
2 | 216
3 | 244
4 | 253
5 | 244
6 | 216
7 | 175
8 | 127
9 | 78
10 | 37
11 | 9
12 | 0
13 | 9
14 | 36
15 | 78
Time | Index | Base | Delta | Offset*Delta | Base + Offset*Delta
0 | 0000.0000 | 127 | 175-127 = 48 = 110000 | 0.0000*110000 = 00000.0000 | 127+0 = 127
1 | 0001.1011 | 175 | 216-175 = 41 = 101001 | 0.1011*101001 = 11100.0011 | 175+28 = 203
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 

## Slide 16: Practice
0 | 127
1 | 175
2 | 216
3 | 244
4 | 253
5 | 244
6 | 216
7 | 175
8 | 127
9 | 78
10 | 37
11 | 9
12 | 0
13 | 9
14 | 36
15 | 78
Time | Index | Base | Delta | Offset*Delta | Base + Offset*Delta
0 | 0000.0000 | 127 | 175-127 = 48 = 110000 | 0.0000*110000 = 00000.0000 | 127+0 = 127
1 | 0001.1011 | 175 | 216-175 = 41 = 101001 | 0.1011*101001 = 11100.0011 | 175+28 = 203
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  |