## Slide 1: ECE 383 – Embedded Computer Systems II Lecture 10 – Datapath and Control
Capt Jeffrey Falkinburg Room 2E46C 333-7366
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Generics
Datapath and Control
Design Process
  If
  For
  While
  Assignment
Basic Building Blocks

## Slide 3: Generics

## Slide 4: Generics – Entity Declaration
Entity Declaration:
    entity lec10 is
    generic (N: integer := 4);
    port( clk: in STD_LOGIC;
    reset : in STD_LOGIC;
    crtl: in std_logic_vector(1 downto 0);
    D: in unsigned (N-1 downto 0);
    Q: out unsigned (N-1 downto 0));
    end lec10;
  Note:
  The variable N is available in the entity and architecture context. In this case, you will need it to define the width of vectors.
  The value of N must be an integer, not a binary string. Just use positive integers for N.

## Slide 5: Generics – Instantiation
  Note:
  The default value for N is 4. That means, if you do not use the generic map statement in the instantiation below, you will get a 4-bit counter.
  The D and Q vectors use N-1 because the vector starts at 0.
Instantiation:
  uut: lec10
  generic map(5)
  port map ( clk => clk,
  reset => reset,
  crtl => crtl,
  D => D,
  Q => Q);

## Slide 6: Generics – 5-Bit Counter
In this case, I made a 5-bit counter. The testbench linked on Lesson 10runs the counter through all four control modes and even shows how it rolls over (around 7.5uS).
Control | Description
00 | Hold
01 | Count up mod 10
10 | Load D
11 | Synchronous Reset

## Slide 7: Datapath and Control

## Slide 8: Datapath and Control
Datapath and Control Design Methodology
  Datapath - responsible for sequencing the actions of the datapath
  Control - responsible for sequencing the actions of the datapath
Fig 10.0 - An abstract digital system constructed from a datapath and a control unit.

## Slide 9: Design Process

## Slide 10: Design Process
Building digital systems using the datapath and control approach is a three-step process.
  Write an algorithmic description for the solution to the problem.
  Parse the algorithmic description into datapath building blocks and control states.
  Define the MIEs and OEs for the control unit.

## Slide 11: mini-C
The programming language used to formalize an algorithmic solution to design problem is referred to as mini-C (a derivative of the C-programming language)
  IF
    if (condition) then BODY_1 else BODY_2
  FOR
  for (i=A; i<B; i += 1)
  WHILE
  while(condition) BODY
  ASSIGNMENT
  X = value

## Slide 12: Design Process – If/Then/Else
Fig 10.1 - The datapath and control components required to realize an if/then/else structure.

## Slide 13: Design Process – For Loop
Fig 10.2 - The datapath and control components required to realize a for loop.

## Slide 14: Design Process – While Loop
Fig 10.3 - The datapath and control components required to realize a while statement.
Bitwise xor operation
Bitwise xor operation

## Slide 15: Design Process – Assignment
Fig 10.5 - The datapath and control components required to realize an assignment statement of the form X=X+Y.

## Slide 16: Basic Building Blocks

## Slide 17: Basic Building Blocks
Table 10.6 - The list of all the basic building blocks and some of their attributes.

## Slide 18: Lesson Outline
Generics
Datapath and Control
Design Process
  If
  For
  While
  Assignment
Basic Building Blocks