## Slide 1
ECE 383 – Embedded Computer Systems II Lecture 9 – Finite State Machines
1
Maj Jeffrey Falkinburg Room 2E46E 333-9193

## Slide 2: Lesson Outline
D Flip Flop
Finite State Machine
FSM Timing
The DAISY System

## Slide 3: D Flip Flop

## Slide 4
Figure 2.66 Circuit delay
Delay
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 5
Figure 2.67 Propagation and contamination delay
Propagation Delay and Contamination Delay
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 6
Figure 2.68 Short path and critical path
Copyright © 2013 Elsevier Inc. All rights reserved.
Critical Path and Shortest Path

## Slide 7
Figure 2.69 Critical and short path waveforms
Copyright © 2013 Elsevier Inc. All rights reserved.
Critical Path and Shortest Path Waveform

## Slide 8: D Flip Flop
Setup time(tsu) - is the amount of time before the rising edge of the clock in which the data inputs must be stable.
Hold time(th) is the amount of time after the rising edge of the clock during which the data input must be stable.
Propagation Delay(tp), is the amount of time after the rising edge of the clock required for the new Q value to become valid.
  It is also known as tCQ, for "time clock to Q", or tFF. These time values are illustrated in the picture below.

## Slide 9: D Flip Flop

## Slide 10
Figure 3.39 Maximum delay for setup time constraint
Time Clock to Q
Propagation Delay
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 11
Figure 3.40 Minimum delay for hold time constraint
Time Clock to Q
Contamination Delay
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 12: D Flip Flop
What type of D Flip Flop is this?
Fill in waveform!
Tsu, Th, Tpd

## Slide 13: Finite State Machine

## Slide 14: Finite State Machine
Finite State Machine (FSM) – most general form of a sequential circuit, a circuit whose output is a function of input and an internal state
Moore or Mealy?

## Slide 15: Finite State Machines
FSM – M- inputs, N – Outputs, and K - bits of state
  FSMs have K registers that can be one of a finite number (2K) unique states
Two types of FSMs?
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 16: Finite State Machines - Moore Machine
Moore Machine – outputs depend only on current state of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 17: Finite State Machines - Mealy Machine
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 18: Finite State Machines - Design
How to Design a State Machine:
  0) Description
  1) State Transition Diagram
  2) State Transition Table & Output Table
  3) Next State and Output State Equations
  4) Schematic
Copyright © 2013 Elsevier Inc. All rights reserved.

## Slide 19: Finite State Machine - Design
Design of a FSM requires three questions answered:
  What are the Memory Input Equations (MIEs)?
  What are the Output Equations (OEs)?
  How many D flip flops are required?

## Slide 20: Finite State Machines - Moore vs Mealy Machine
Moore Machine – outputs depend only on current state of the machine.
Mealy Machine – outputs depend on both the current state and current inputs of the machine.
20
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N
Combinational Logic or
Next State Logic
Flip Flops
Output Logic
Inputs
Outputs
Current
State
Next
State
Clock
M
K
K
N

## Slide 21: Finite State Machine
Figure 10.1 Block diagram of an FSM.

## Slide 22: FSM Timing

## Slide 23: FSM Timing
Event 1- Since flip flops sample their inputs on the positive edge of the clock, this point is the beginning of the timing analysis.

## Slide 24: FSM Timing
Event 2 - The propagation delay of the flip flops means a small delay occurs between the clock edge and the flip flop outputs, Q, becoming valid. This is the called the propagation delay of the flip flop and denoted T_ff in the diagram below.

## Slide 25: FSM Timing
Event 3 - In order to maximize the clocking frequency of the FSM, the new inputs, X, to the FSM should be applied at the same moment that the flip flop outputs become valid.

## Slide 26: FSM Timing
Event 4 - According to Figure above, changing Q and X causes the memory inputs to change (the Y signal above). The delay between the application of the new inputs to the MIE logic and Y becoming valid is the propagation delay of the combination logic, denoted Tcombo.

## Slide 27: FSM Timing
Event 5 - When the Y values are valid, a small delay occurs while the flip flops register their new inputs, denoted Tsu. After this setup time, the FSM is ready for another clock edge.

## Slide 28: The DAISY System
Lets bring in the cows.

## Slide 29: The DAISY System
Dairy Automated Information System, or DAISY for short
Word Statement Cows have a RFID tag attached to their collars. When the cow passes through the cattle chute on their way into the barn, a RFID reader reads the unique ID stored on the RFID tag and logs the cow into the barn.
  The RFID system outputs a single bit: a 1 means the system has read an RFID tag and has successfully checked a cow back into the barn; a 0 means the RFID system is either still processing a tag or is not currently reading a tag.
  The RFID system outputs a single bit:
    Logic 1 – Cow Checked In
    Logic 0 – Cow Not Processed

## Slide 30: The DAISY System
In order to ensure each cow is scanned, the flow of cows into the barn is controlled by two gates at either end of the chute. Each gate is controlled by a single bit. To lift a gate, this input must be held at logic 1; to lower a gate, the input must be held at a logic 0. The sequence of raising and lowering the gates in order to control the flow of cows.
  Flow of cows is controlled by two gates
    Logic 1 – To lift a gate
    Logic 0 – To lower a gate

## Slide 31: The DAISY System
Step 1 - Gate1 is lifted allowing cow A to enter the chute.

## Slide 32: The DAISY System
Step 2 - The DAISY system has detected cow A is in the chute and closes gate1.

## Slide 33: The DAISY System
Step 3 - The cow waits in the closed off chute until the RFID reader signals that it has read the tag and checked in cow A.

## Slide 34: The DAISY System
Step 4 - Gate2 is raised allowing cow A to leave. If the cow takes more than 30 seconds to leave, then the cow is "goosed" by a three-second burst of compressed air. An air bust is repeated at 30-second intervals until the cow leaves the chute. At any time when the cow leaves the chute, Gate 2 is closed and the system transitions back to Step 1.

## Slide 35: The DAISY System

## Slide 36: The DAISY System
DAISY FSM Entity

## Slide 37: The DAISY System
Inputs to Daisy
Outputs to Daisy
RFID Scanner = r | Cow Present = c | Timer Status = t
1 - Cow checked in | 1 - cow present | 1 - timer up
0 - Cow not processed | 0 - no cow | 0 - timer running
Gate1 | Gate2 | Timer Control | Air Valve
1-gate up | 1-gate up | 00 Stop timer | 0 closed
0-gate down | 0-gate down | 01 Set to 30 secs | 1 open
 |  | 10 Set to 3 secs | 
 |  | 11 Run timer | 

## Slide 38: The DAISY System
State Diagram
  Open gate1
  Wait for cow to enter chute
  Close gate1
  Wait for RFID to read cow
  Open gate2
  Wait for cow to leave
  If 30 seconds has transpired, then "goose" cow; goto Step 6
  Else if the cow has left, then close gate2; goto Step 1

## Slide 39: The DAISY System
Memory Input Equations
How many Flip Flops do we need?
State | Code
WaitEnter | 000
WaitRead | 001
Set30 | 010
WaitLeave | 011
Set3 | 100
Goose | 101

## Slide 40: The DAISY System
Solve for three (one for each flip flop) 6-input Boolean Expressions
  Using espresso

## Slide 41: The DAISY System – Expresso input file
.i 6 # .i specifies the number of inputs
.o 3 # .o specifies the number of outputs
.ilb Q2 Q1 Q0 R C T # This line specifies the names of the inputs in order
.ob D2 D1 D0 # This line specifies the names of the outputs in order
# The first six digits (before the space) correspond
# to the inputs, the three after the space correspond
# to the outputs, both in order specified above.
000 -0- 000 # WaitEnter + c' => WaitEnter
000 -1- 001 # WaitEnter + c => WaitRead
001 0-- 001 # WaitRead + R' => WaitRead
001 1-- 010 # WaitRead + R => Set30
010 --- 011 # Set30 => WaitLeave
011 -10 011 # WaitLeave + T'C => WaitLeave
011 -11 100 # WaitLeave + TC => Set3
011 -0- 000 # WaitLeave + c' => WaitEnter
100 --- 101 # Set3 => Goose
101 --0 101 # Goose + T' => Goose
101 --1 010 # Goose + T => Set30 .e # Signifies the end of the file.

## Slide 42: The DAISY System – Expresso Output

## Slide 43: The DAISY System – One’s Hot Encoding
Using a One’s Hot Encoding MIEs:
D_WaitEnter = Q_WaitEnter * c' + Q_WaitLeave * c'
D_WaitRead = Q_WaitRead * r' + Q_WaitEnter * c
D_Set30 = Q_WaitRead * r + Q_Goose * t
D_WaitLeave = Q_Set30 + Q_WaitLeave * t' * c
D_Set3 = Q_WaitLeave * t * c
D_Goose = Q_Goose * t' + Q_Set3
State | Code
WaitEnter | 000001
WaitRead | 000010
Set30 | 000100
WaitLeave | 001000
Set3 | 010000
Goose | 100000

## Slide 44: The DAISY System – Output Equations
The first step in generating the output equations is to build a control word table - a table listing, for each state, its output.
State | Gate1 | Gate2 | Timer | Control Air
 | 1-gate up | 1-gate up | 00 Stop timer | 0 - closed
 | 0-gate down | 0-gate down | 01 Set to 30 secs | 1 - open
 |  |  | 10 Set to 3 secs | 
 |  |  | 11 Run timer | 
WaitEnter | 1 | 0 | 00 | 0
WaitRead | 0 | 0 | 00 | 0
Set30 | 0 | 1 | 01 | 0
WaitLeave | 0 | 1 | 00 | 0
Set3 | 0 | 1 | 10 | 0
Goose | 0 | 1 | 11 | 1

## Slide 45: The DAISY System – Output Equations
Z_Gate1 <= Q_WaitEnter;
Z_Gate2 <= Q_Set30 + Q_WaitLeave + Q_Set3 + Q_Goose
Z_Timer_1 <= Q_Set3 + Q+Goose
Z_Timer_0 <= Q_Set30 + Q_Goose
Z_Air = Q_Goose

## Slide 46: The DAISY System – VHDL