## Slide 1
ECE 383 – Embedded Computer Systems II Lecture 13 – Lab 2 – Data Acquisition, Storage and Display
1

## Slide 2: Lesson Outline
Time Logs!
Lab 2 – Data Acquisition, Storage and Display

## Slide 3: Lab 2 – Data Acquisition, Storage and Display

## Slide 4: Lab 2 – Lab Overview
Lab Overview - Integrate the video display controller developed in Lab 1 with the audio codec on the Nexys Video board to build a basic 2-channel oscilloscope.

## Slide 5: Lab 2 – Connections

## Slide 6: Lab 2 – Connections
Buttons
Power
HDMI Out
USB Prog
CPU Reset
Audio
Input
Audio
Output
JB PMOD
Connector
For Test Signals

## Slide 7: Lab 2 – Architecture

## Slide 8: Lab 2 – Architecture

## Slide 9: Lab 2 – ADAU1761 SigmaDSP Audio Codec
Analog Devices ADAU1761 SigmaDSP Audio Codec.
  http://www.analog.com/media/en/technical-documentation/data-sheets/ADAU1761.pdf
1. Loop back L_bus_out and R_bus_out and listen on the HP_OUT Jack
  process (clk)
  begin
  if (rising_edge(clk)) then
  if reset_n = '0' then
  L_bus_in <= (others => '0');
  R_bus_in <= (others => '0');
  elsif(ready = '1') then
  L_bus_in <= L_bus_out;
  R_bus_in <= R_bus_out;
  end if;
  end if;
  end process;

## Slide 10: Lab 2 – ADAU1761 SigmaDSP Audio Codec
Input Value |  | Ouput Value | 
2's complement | 2's value | unsigned | unsigned value
100...000 | -131072 | 000...000 | 0
111...111 | -1 | 011...111 | 131071
000...000 | 0 | 100...000 | 131072
000...001 | 1 | 100...001 | 131073
011...111 | 131071 | 111...111 | 262143
2. Convert L_bus_out signal is to send it, in an unsigned format, to be stored in the block ram (BRAM).

## Slide 11: Lab 2 – Datapath
entity lab2_datapath is
Port( clk : in STD_LOGIC;
reset_n : in STD_LOGIC;
ac_mclk : out STD_LOGIC;
ac_adc_sdata : in STD_LOGIC;
ac_dac_sdata : out STD_LOGIC;
ac_bclk : out STD_LOGIC;
ac_lrclk : out STD_LOGIC;
scl : inout STD_LOGIC;
sda : inout STD_LOGIC;
tmds : out STD_LOGIC_VECTOR (3 downto 0);
tmdsb : out STD_LOGIC_VECTOR (3 downto 0);
sw: out std_logic_vector(2 downto 0);
cw: in std_logic_vector (2 downto 0);
btn: in STD_LOGIC_VECTOR(4 downto 0);
exWrAddr: in std_logic_vector(9 downto 0);
exWen, exSel: in std_logic;
Lbus_out, Rbus_out: out std_logic_vector(15 downto 0);
exLbus, exRbus: in std_logic_vector(15 downto 0);
flagQ: out std_logic_vector(7 downto 0);
flagClear: in std_logic_vector(7 downto 0));
end lab2_datapath;

## Slide 12: Lab 2 – Flag Register
entity flagRegister is
Generic (N: integer := 8);
Port( clk: in STD_LOGIC;
reset_n : in STD_LOGIC;
set, clear: in std_logic_vector(N-1 downto 0);
Q: out std_logic_vector(N-1 downto 0));
end flagRegister;
reset_n | clk | set | clear | Q+
0 | X | X | X | 0
1 | 0,1,falling | X | X | Q
1 | rising | 0 | 0 | Q
1 | rising | 1 | 0 | 1
1 | rising | 0 | 1 | 0
1 | rising | 1 | 1 | X

## Slide 13: VHDL Package file
Packages – Package for Lab 2
  http://ece.ninja/383/lecture/code/lab2_pack.vhdl
This is where you will put all your component declarations
Include this at the top of your file:
use work.lab2Parts.all; -- all my components are declared here

## Slide 14: VHDL Code
Overall Lab 2 File: lab2.vhd
  Lab 2 Datapath: Lab2_datapath_tb.vhd
  Audio Codec Wrapper: Audio_Codec_Wrapper.vhd (Audio Codec Wraper for Xilinx Vivado)
    i2s_ctl.vhd (I2S Transmitter portion of Audio Codec Wraper for Xilinx Vivado)
    audio_init.v (Audio Initializer portion of Audio Codec Wraper for Xilinx Vivado)
    TWICtl.vhd (TWI Controller portion of Audio Codec Wraper for Xilinx Vivado)
    You need to add a clocking wizard for the Audio Codec and set the output frequencies to what is required (see comments in the Audio Codec Wrapper file).
Constraint file: Lab2.xdc

## Slide 15: Lab 2 – Generating Audio Waveforms
Since you need to use a 3.5mm jack to input signals to the Nexys Video board, your phone's audio output works quite well. However, make sure you get an app where you can control both the left and right audio channels individually (i.e. the green and yellow signals in the figure above). The Keuwl Dual Channel Function Generator (available on Google Play) works well for Android Phones, and is easy to use once you get the hang of it.

## Slide 16: Lab 2 – Requirements Gate Check 1
Gate Checks for Required Functionality
  There are 2 gate checks associated with this lab, each worth 5 points - see the rubric below.
Gate Check 1
  By COB Lesson 13, you must have started a Lab 2 Vivado project and downloaded the template files and drop in your Video, VGA, Scopeface, dvid, and tdms files from Lab 1 into your Lab 2 project in order to test your Lab 1 Scopeface works when you implement you Audio Code Wrapper. Notice from the block diagram…you will copy your Video instantiation and button processes from Lab 1 into your Lab 2 Datapath. You will also have to re-implement the Lab 1 Clocking Wizard in you Lab 2 project. Doing this will eliminate a lot of errors from un-driven output signals on lab 2 top.

## Slide 17: Lab 2 – Requirements Gate Check 1
Gate Check 1
  Next, you will need to have implement another Clocking Wizard and the Audio Codec Wrapper inside the Datapath entity to get your Audio Codec to begin functioning. Once you fully implement the Audio Codec Wrapper, you will drop in the Loopback process and make connections to loopback the serial ADC input back out to the DAC output (i.e. send the signal back into the Codec). Once you implement the design on the board, you can verify functionality by applying an audio signal to the audio line in jack (blue) and listening to it on the audio line out jack (Green) using a standard oscilloscope. Additionally your Scopeface and Button inputs from Lab 1 should be functional as well.

## Slide 18: Lab 2 – Requirements Gate Check 2
Gate Check 2
  NOTE: THIS IS THE HARDEST PART! By BOC Lesson 15, you must have implemented and connected the left channel BRAM and BRAM Address Counter to write Audio Codec data to BRAM. Once implemented, you can verify your BRAM works by using the given datapath testbench and watching the BRAM write address increment and data be written/read from the BRAM.

## Slide 19: Lab 2 – Requirements Gate Check 2 Cont
Gate Check 2
  Once this is working, you must implement Video entity (from Lab 1) to take the left channel output from BRAM and send it to the Channel 1 waveform to be displayed when the readL value equals the row value. Once implemented, this functionality can be verified first with the given datapath testbench to verify the channel 1 values are being updated properly when readL equals the row value. Additionally, you may try to implement this on the hardware and verify that your scopeface is still present and some values are being displayed for Channel 1 (at this point the waveform will be scrolling across the display or may be scaled wrong).

## Slide 20: Lab 2 – Requirements Required Functionality
Required Functionality
  Get a single channel of the oscilloscope to display with reliable triggering that holds the waveform at a single point on the left edge of the display. A 220Hz waveform should display something similar to what is shown in the screenshot at the top of this page. Additionally, you must have the following done:
    Use a package file to contain all your component declarations.
    Use separate datapath and control unit.

## Slide 21: Lab 2 – Requirements Required Functionality Cont 1
Required Functionality
    Your datapath must use processes which are similar to our basic building block (counter, register, mux, etc.). I do not want to see one massive process that attempts to do all the work in the datapath.
    Testbench for the flagRegister.
    Testbench for the control unit.

## Slide 22: Lab 2 – Requirements Required Functionality Cont 2
Required Functionality
    Testbench for the datapath unit showing data (different value than what is given in the testbench) coming out of the audio codec and being converted from signed to unsigned and then to std_logic_vector to go into your BRAM. Include calculations to back up what the waveform shows.

## Slide 23: Lab 2 – Requirements Required Functionality Cont 3
Required Functionality
    For Bonus Points: Testbench for the datapath unit showing that same data coming out of the BRAM. Make sure you show the read address and the data values coming out. This will require you to set your control words on the testbench. Additionally, you will have to drive the pixel_clock on the Video Module. Once you get the datapath testbench running you will notice that DCM module doesn't put out a clock in the Video Module.

## Slide 24: Lab 2 – Requirements B-Level Functionality
B-level Functionality
  Meet all the requirements of required functionality
  Add a second channel (in green).
  Integrate the button debouncing strategy in HW #7 (or another equivalent debouncing method) to debounce the buttons controlling the trigger time and trigger voltage.
  Move the cursors on the screen.

## Slide 25: Lab 2 – Requirements A-Level Functionality
A-level Functionality
  Meet all the requirements of B-level functionality.
  Use the trigger voltage marker to establish the actual trigger voltage used to capture the waveform. As the trigger is moved up and down, you should see the point at which the waveform intersects the left side of the screen change.

## Slide 26: Lab 2 – Requirements Turn In
Turn In Requirements
  All your work in this lab is to be submitted using Bitbucket. The main part of the lab is your README, documenting your design. Your README must include the following:
  Introduction - Provide a brief overview of the problem.
  Implementation - Provide block-diagram of your solution using the signal names in your code. The block diagram given above is somewhat incomplete, so make sure to include corrections to it. For each module that you built, explain its overall purpose, inputs, outputs, and behavior. Include all your vhdl files (code and testbench), wcfg file, and bit files. Put these in a folder called "code".

## Slide 27: Lab 2 – Requirements Turn In Cont 1
Turn In Requirements
  Test/Debug - Briefly describe the methods used to verify system functionality.
  List the major problems you encountered and how you fixed them. This should cover all the problems you encountered in the lab and how you fixed them. Break each problem and solution into separate paragraphs.
  Capability - Well you have built a oscilloscope, what are its capabilities?
    The horizontal axis represents time. There are 10 major divisions on the display; how long does each major division represent?

## Slide 28: Lab 2 – Requirements Turn In Cont 2
Turn In Requirements
  Capability Continued -
    Each major time division is split into 4 minor division, how long does each minor division represent?
    Generate a sine wave that can be fully captured on your display (like the yellow channel in the image at the top of this web page). record its height in major and minor vertical divisions. Measure this same audio output using the break out audio cable. Record the peak-to-peak voltage. Compute the number of volts in each major and minor vertical division.

## Slide 29: Lab 2 – Requirements Turn In Cont 3
Turn In Requirements
  Capability Continued -
    Starting at address 0, how long does it take to fill the entire memory with audio samples (coming in at 48kHz)?
    How long does it take to completely draw the display once?
    The question is likely relevant to Lab 3 - how long is the vsynch signal held low?
  Conclusion - Explain what your learned from this lab and what changes you would recommend in future years to this lab or the lectures leading up to this lab.