## Slide 1
ECE 383 – Embedded Computer Systems II Lecture 19 – Lab 3 – Software control of a datapath
1

## Slide 3: Lesson Outline
Time Logs!
Lab 3 – Software control of a datapath

## Slide 4: Lab 3 – Software control of a datapath

## Slide 5: Lab 3 – Lab Overview
Lab Overview - In this lab we will integrate the video display controller developed in Lab 2 with the MicroBlaze processor built using the fabric of the FPGA. In the preceding lecture we have learned about the SDK tool chains, now its time to put that knowledge to the test by building a software controlled datapath. Lab 2 revealed some shortcomings of our oscilloscope that this lab intends on correcting.
  Using both trigger volt and trigger time for trigger
  Using polling and/or interrupts
  Ability to enable and disable channels to display
  Ability to trigger off channel 2
  Ability to change the slope direction for the trigger.

## Slide 6: Lab 3 – Lab Overview
The following figure shows required functionality - your program should allow the user to change the position of the triggerVolt and triggerTime indicators with the result that the waveform should be drawn so that the periodic waveform is increasing through that voltage at that time.

## Slide 7: Lab 3 – Connections
Buttons
Power
HDMI Out
USB Prog
CPU Reset
Audio
Input
Audio
Output
JB PMOD
Connector
For Test Signals
USB UART

## Slide 8: Lab 2 – Architecture

## Slide 9: Lab 3 – Architecture
axi_uartlite_0 @ 40600000
S_AXI_ACLK
S_AXI_ARESETN
slv_reg0  31
To/From Microblaze
clk
reset_n
Lab2 Signals
Artix 7 (design_1 for Lab 3)
MicroBlaze
my_oscope_ip_v2_0.vhd @ 0x44a00000
my_oscope_ip_v2_0_S00_AXI.vhd
Lab2_dp.vhd
32x32
Lab2.xdc
Nets to Pins
Pins off
chip
Design_1.xdc
AA19
V18
RX
RX
TX
TX
clk
reset_n
R4
G4
ready
myISR()
main()
Lab3.c
Interrupt
axi_lite
Signals going In/Out of Artix 7 Chip
Lab2_fsm.vhd
cw
sw

## Slide 16: Lab 3 – UART Note
Note: In your program, you may want to check if the users has hit the key on the keyboard without having to actually read the key. For these cases the following command will prove useful. Note that "uartRecReg" is a constant, the address of the uart.
XUartLite_IsReceiveEmpty(uartRecReg);

## Slide 17: Lab 3 – Hardware
With the expectation of the following engineering change orders (ECO) in the table below, the hardware you developed in lab2 will be unchanged. For the following ECO, please refer to the high-level architecture in lab 2.
Name: | Trigger Voltage, Trigger Time
Scope: | lab2_dp and lab2
Type: | Change to the entity descriptions.
Details: | Inside the lab2_dp component, remove the logic driving the triggerVolt and triggerTime signals into the video component. Remove the buttons signal from the lab2 and lab2_dp entities. Remove the buttons signal from the ucf file. Add the triggerVolt and triggerTime signals to the lab2 and lab2_dp entity descriptions. Drive the triggerTime and triggerVolt inputs on the video component with the corresponding signals on the lab2_dp entity.
(or Option for 2021: Keep lab 2 buttons, and input Trigger Volt and Time
Into Microblaze using slv_regs

## Slide 18: Lab 3 – Signals
Your first step will be to create a component for your lab2 component in your Vivado repository. This will require you to think about what signals are routed to the MicroBlaze and those going outside the Artix 7 chip.
To/From MicroBlaze | Outside Artix 7
exWrAddr | clk
exWen | reset
exSel | ac_mclk
L_bus_out, R_bus_out | ac_adc_sdata
exLbus, exRbus | ac_dac_sdata
flagQ | ac_bclk
flagClear | ac_lrclk
triggerTime | sda
triggerVolt | scl
ready | tmds
Ch1_enb, Ch2_enb ? | tmdsb

## Slide 19: Lab 3 – Software
All the memory mapped hardware registers will have their names setup as #define's with a name ending in "Reg".
Any register with bit fields will have the bit index setup as #define's with a name ending in "Bit".
The flagQ and flagClear registers need to be at the same address.

## Slide 20: Lab 3 – Requirements Gate Check 1
Gate Check 1
  By the conclusion of lesson 22, you need to have all of your Lab 2 functionality implemented with the Microblaze.
  That is, you need to export your Lab 2 design into the SDK and be able to achieve the same functionality as you did in Lab 2.

## Slide 21: Lab 3 – Requirements Gate Check 2
Gate Check 2
  By the conclusion of lesson 23, you need to be able to send UART commands to your FPGA to adjust the trigger on the screen. The trigger on the screen should properly react to moving the trigger either up or down.
(or Option for 2021: Keep lab 2 buttons, and input Trigger Volt and Time
Into Microblaze using slv_regs. Show on UART display you can
read Trigger Volt and Time

## Slide 22: Lab 3 – Requirements Required Functionality
Required Functionality
  In order to make required functionality you will need to properly trigger the oscilloscope on channel 1 using a positive edge trigger. Control of this process is to be performed using the MicroBlaze. The main tasks of the MicroBlaze will include:
    Moving audio samples into a pair of circular buffer. These circular buffers will be maintained in the address space of the MicroBlaze. That is you should have two big arrays defined in your program. Use polling of the ready bit of the flag register.
    Examining the samples looking for a trigger event.
    Fill the remaining sample slots in memory.
(or Option for 2021: You can use a Linear Buffer instead of a Circular Buffer

## Slide 23: Lab 3 – Requirements Required Functionality Cont 1
Required Functionality cont
    Move the appropriate buffer values into the display memory of the oscilloscope (lab2) component.
    Provide a user menu (through the terminal) allowing the user to adjust the trigger voltage and trigger time.
(or Option for 2021: Keep lab 2 buttons, and input Trigger Volt and
Time into Microblaze using slv_regs. Show on UART display you can
read Trigger Volt and Time

## Slide 24: Lab 3 – Requirements
B-level Functionality A-level Functionality
  Achieve required functionality.
  [10-points] Use the ready bit of the flag register to trigger an interrupt. The ISR should store the samples (left and right), look for a triggering even, and signal when the stored samples should be transferred to the BRAM in the oscilloscope component.
  [5-points] Add means to control Ch1_enb and Ch2_enb either by adding two FPGA board switches or controlled by microblaze terminal interface.

## Slide 25: Lab 3 – Requirements
A-level Functionality
  Ability to trigger off channel 2
  Ability to change the slope direction for the trigger.

## Slide 26: Lab 3 – Requirements Turn In
Turn In Requirements
  All your work in this lab is to be submitted using Bitbucket
  README: only needs
    Design
      Slide 9 diagram (no change?)
      Updated lab2 block diagram with correct signals
      Mapping of 32 AXI registers to lab2 signals
    Evidence of completing Gate Checks 1 and 2, basic functionality, and A-functionality, along with the date/time achieved
    Issues and lessons learned

## Slide 27: Dummy Waveforms for Testing
Audio_Codec_Wrapper has sim_live
  Use switch or C-doe to toggle sim_live?
Walk through example C-code test commands