## Slide 1: ECE 383 – Embedded Computer Systems II Lecture 3 – Combinational Element, unsigned, UCF file, synthesis
Capt Jeffrey Falkinburg Room 2E46C 333-7366
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Synthesis
UCF file
Combinational Element
Unsigned Numeric Standard
Combinations

## Slide 3
pp 284
http://www.xilinx.com/support/documentation/user_guides/ug385.pdf

## Slide 4: Synthesis

## Slide 5: Synthesis
Insert this code into your Majority.ucf file
  Inputs from switches and outputs to LEDs
# This is slide switch SW0
NET "a" LOC = A10;
# This is slide switch SW1
NET "b" LOC = D14;
# This is slide switch SW2
NET "c" LOC = C14;
# This is LED LD0
NET "f" LOC = U18;

## Slide 6: UCF file

## Slide 7: UCF file
Atlys Master UCF
  http://ece.ninja/383/datasheets/AtlysGeneral.ucf

## Slide 8: Combinational Element

## Slide 9: Combinational Element – Common error
Common error that may come up in your designs
You cannot use a variable listed on the entity as an out port, on the right hand side of a signal assignment statement.
  entity circuit is
  port (clk, data: in std_logic;
  q, not_q: out std_logic);
  end circuit;
  architecture error of circuit is
  begin
  q <= some cool logical stuff using clk and data;
  not_q <= not q;
  end error;

## Slide 10: Combinational Element – Solution
Solution
assign "some cool logical stuff using clk and data" to a temporary variable
  entity circuit is
  port (clk, data: in std_logic;
  q, not_q: out std_logic);
  end circuit;
  architecture error of circuit is
  signal temp std_logic;
  begin
  temp <= some cool logical stuf using clk and data;
  q <= temp;
  not_q <= not temp;
  end error;

## Slide 11: Combinational Element - Mux
Simplify muxes using conditional signal assignment statement
Example:
  x <= y0 when S = "00" else
  y1 when S = "01" else
  y2 when S = "10" else
  y3;
Draw this Circuit assuming 8-bit inputs
Now build 4-1 mux w/ 2-1 muxes

## Slide 12: Unsigned Numeric Standard

## Slide 13: Unsigned Numeric Standard
So far we mostly used STD_LOGIC_1164 library
  library IEEE;
  use IEEE.STD_LOGIC_1164.all;
  Library Contents: http://www.csee.umbc.edu/portal/help/VHDL/packages/std_logic_1164.vhd

## Slide 14: Unsigned Numeric Standard
Numeric_Std Library supports 2 main datatypes
  Signed and Unsigned
  Library Contents: http://www.csee.umbc.edu/portal/help/VHDL/packages/numeric_std.vhd
  library IEEE;
  use IEEE.std_logic_1164.all;
  use IEEE.NUMERIC_STD.ALL;
  entity lec3 is
  port( au, bu: in unsigned(3 downto 0);
  cu,du,su: out unsigned(3 downto 0);
  as, bs: in signed(3 downto 0);
  cs,ds,ss: out signed(3 downto 0));
  end lec3;

## Slide 15: Unsigned Numeric Standard
  architecture structure of lec3 is
  begin
  cu <= "1000" when (au > bu) else
  "0110" when (au = bu) else
  "0001";
  su <= au + bu;
  du <= au - bu;
  cs <= "1000" when (as > bs) else
  "0110" when (as = bs) else
  "0001";
  ss <= as + bs;
  ds <= as - bs;

## Slide 16: Unsigned Numeric Standard
Unsigned
Signed
A | B | Value A | Value B | A >? B | A =? B | A <? B | A + B | A - B
0010 | 0100 |  |  |  |  |  |  | 
1011 | 0001 |  |  |  |  |  |  | 
0110 | 1010 |  |  |  |  |  |  | 
0111 | 1000 |  |  |  |  |  |  | 
A | B | Value A | Value B | A >? B | A =? B | A <? B | A + B | A - B
0010 | 0100 |  |  |  |  |  |  | 
1011 | 0001 |  |  |  |  |  |  | 
0110 | 1010 |  |  |  |  |  |  | 
0111 | 1000 |  |  |  |  |  |  | 

## Slide 17: Unsigned Numeric Standard

## Slide 18: Unsigned Numeric Standard
You will typically use STD_LOGIC_VECTOR and UNSIGNED
You may need to convert between the two
  a: std_logic_vector(7 downto 0);
  b: unsigned(7 downto 0);
  c: std_logic_vector(7 downto 0);
  b <= unsigned(a);
  c <= std_logic_vector(b);

## Slide 19: Combinations

## Slide 20: Combinations
Common Combinations if/then/else
All conditional statements consist of three parts:
  the condition to be checked (the if clause)
  the statement to be evaluated when the condition is true (the then clause)
  the statement to be evaluated when the condition is false (the else clause)
Typically, the condition being evaluated seeks the relative magnitude of two unsigned binary numbers, requiring a comparator.
The then and else clauses will typically require some logic or arithmetic operation

## Slide 21: Combinations
In order to illustrate the hardware realization of a conditional statement, consider the following example:
  C: if (a<4) then z=y+3 else z=y+7
  VHDL: z <= y+3 when (a < 4) else y+7;

## Slide 22: Combinations
However, this circuit is not minimal, one of the adders can be removed.
How?
Practice on Homework

## Slide 23: Lesson Outline
Synthesis
UCF file
Combinational Element
Unsigned Numeric Standard
Combinations